## Slide 1: HydroSentinel AI
Five-level flood-risk alerts from IT2FIS, PSO, SOM and ANFIS, compared on real river data
Soft Computing project review · version 0.6 · October 2026
Live demo: floodguard-ai-chi.vercel.app
Notes: Introduce the project in one sentence: four soft-computing techniques each issue a five-level flood alert with a reason, and we test how good and how robust those alerts are on held-out river data. The five squares are the alert levels used throughout: Normal, Low, Moderate, High, Critical.

## Slide 2: Why this project
1
Sensors fail
Gauges go missing, freeze, spike or disagree, and an alarm built on a bad reading is a false alarm or a missed flood.
2
Alerts must be explained
A flood warning that cannot say why it was raised is hard to trust or act on.
3
Which technique works?
Expert fuzzy rules, optimisation, unsupervised maps and neuro-fuzzy learning have never been compared like-for-like here.
Research questions
Q1
Which of IT2FIS, PSO-tuned IT2FIS, SOM and ANFIS gives the best five-level alerts?
Q2
Does PSO tuning improve the expert IT2FIS, or only fit the validation data?
Q3
How do the models cope with faulty sensors, and does a reliability layer help?
Notes: Three motivations, three research questions. Every result later in the deck answers one of Q1 to Q3.

## Slide 3: Real river data, fully traceable
Bengalas River, Brazil (primary)
72,011
records
30 min
sampling
2019–23
period
Water level [m], station rain gauge and a 504-cell weather-radar grid. Station 221342310, Petrópolis, RJ. Soares et al., Transactions in GIS 30(2) e70254 (2026), doi:10.1111/tgis.70254. MIT-licensed repository, SHA-256 checked.
Malwathu Oya, Sri Lanka (check)
4,765
days
daily
sampling
2005–18
period
Water level at Kappachchiya and 6 rain gauges. Rathnayake et al., PLOS ONE 18(4) e0282847 (2023). No dates in the file, so a day index is used. Daily data cannot support sub-daily horizons.
Indian sources (IMD, CWC, India-WRIS, NWDP, CAMELS-IND) were checked: none has open, co-located sub-daily level + rain data.
Notes: Both datasets come from peer-reviewed papers with public repositories; files are checksum-pinned. The Brazilian origin is disclosed: we looked for Indian data first and none offers open sub-daily level plus rainfall. CAMELS-IND is daily only and is the next step.

## Slide 4: Five alert levels from the training data
Normal
< 0.99 m
below μ + 0.5σ
Low
≥ 0.99 m
from μ + 0.5σ
Moderate
≥ 1.14 m
from μ + 1σ
High
≥ 1.43 m
from μ + 2σ
Critical
≥ 1.72 m
from μ + 3σ
ALERT = High or Critical (μ + 2σ is the flood threshold in the source paper's code)
How a label is made (proxy, not a recorded flood)
Label for time t at horizon h = the alert level of the water level actually observed at t + h.
μ and σ come from the training period only; no flood events exist in the data.
Chart: Test-period labels, 1 h ahead (Bengalas)
| Normal | Low | Moderate | High | Critical
test steps | 14672 | 3844 | 1735 | 346 | 307
Notes: Thresholds for Bengalas in metres: 0.993, 1.137, 1.427, 1.716. Only 3.1 % of test steps are alerts, which is why we report precision, recall and F1 rather than accuracy. Labels are proxies: scores measure agreement with this rule, not real-world flood warnings.

## Slide 5: One pipeline, four techniques side by side
Sensors
water level, rain gauges / radar
Reliability layer
optional: check readings, down-weight, fuse
3 inputs
level · rate of rise · rain
IT2FIS
PSO-IT2FIS
SOM
ANFIS
Alert + reasons
Normal … Critical
Chronological split, no shuffling (Bengalas)
Fit block (train 80 %) · 40,325 rows
2019-01 → 2021-10
Validation · 10,082 rows
→ 2022-07
Test (used once) · 21,604 rows
2022-07 → 2023-12
Same inputs, same labels, same split: differences in the results come from the technique itself.
Notes: All four models get exactly the same three inputs, so differences come from the technique. The reliability layer is a switch: off means raw readings, on means each reading is checked and reliability-weighted before the models run. Everything is fitted on the training period; hyper-parameters and PSO use only the validation block; the test period is evaluated once.

## Slide 6: IT2FIS: expert rules with uncertain boundaries
1
Fuzzify
Each input gets a lower and an upper membership grade in each term (level has 5 terms; rise and rain have 4).
2
Fire 80 rules
e.g. IF level is Elevated AND rise is Rising AND rain is Heavy THEN risk is Critical.
3
Type-reduce
Karnik–Mendel gives a risk interval [yl, yr] on a 0–100 scale.
4
Decide
Midpoint → band: 0–20 Normal … 80–100 Critical.
Chart: Fitted level membership functions, Bengalas (x = water level, m)
| 0.56 | 0.59 | 0.61 | 0.64 | 0.67 | 0.69 | 0.72 | 0.75 | 0.77 | 0.80 | 0.82 | 0.85 | 0.88 | 0.90 | 0.93 | 0.96 | 0.98 | 1.01 | 1.04 | 1.06 | 1.09 | 1.12 | 1.14 | 1.17 | 1.20 | 1.22 | 1.25 | 1.28 | 1.30 | 1.33 | 1.36 | 1.38 | 1.41 | 1.44 | 1.46 | 1.49 | 1.52 | 1.54 | 1.57 | 1.60 | 1.62 | 1.65 | 1.68 | 1.70 | 1.73 | 1.76 | 1.78 | 1.81 | 1.84 | 1.86 | 1.89 | 1.92 | 1.94 | 1.97 | 2.00 | 2.02 | 2.05 | 2.08 | 2.10 | 2.13
Normal | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.977 | 0.6088 | 0.2406 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
AboveNormal | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.023 | 0.3912 | 0.7594 | 1 | 1 | 1 | 0.7678 | 0.3996 | 0.0314 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Elevated | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.2322 | 0.6004 | 0.9686 | 1 | 1 | 1 | 1 | 1 | 1 | 0.977 | 0.7929 | 0.6088 | 0.4247 | 0.2406 | 0.0565 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
High | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.023 | 0.2071 | 0.3912 | 0.5753 | 0.7594 | 0.9435 | 1 | 1 | 1 | 1 | 1 | 0.9519 | 0.7678 | 0.5837 | 0.3996 | 0.2155 | 0.0314 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
VeryHigh | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0481 | 0.2322 | 0.4163 | 0.6004 | 0.7845 | 0.9686 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
High: upper MF | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0889 | 0.273 | 0.4571 | 0.6412 | 0.8253 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.8337 | 0.6496 | 0.4655 | 0.2814 | 0.0973 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
High: lower MF | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.1412 | 0.3253 | 0.5094 | 0.6935 | 0.8776 | 1 | 1 | 1 | 0.886 | 0.7019 | 0.5178 | 0.3337 | 0.1496 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Nothing is trained on labels: boundaries come from training statistics, the band from year-to-year variation.
Notes: Solid lines are the embedded Type-1 membership functions of the five level terms; the two grey lines are the upper and lower membership functions of the High term. The gap between them is the footprint of uncertainty: we are not sure exactly where High begins, because the mean + 2 sd boundary varies between training years. We cap the band at half the ramp width; without that cap, a higher level could produce a lower alert, which we found and fixed.

## Slide 7: PSO: tuning where the fuzzy sets sit
What is optimised
11 numbers: a shift for each of the 10 crossover points (4 level, 3 rise, 3 rain; at most 40 % of the gap to a neighbour) and 1 scale for the uncertainty band (0–3×). Rules and inference stay unchanged.
Objective
Validation alert F1 + 0.25 × five-level macro F1, on the last 20 % of the training period, per horizon. The test period is never used.
Swarm
20 particles × 20 iterations; inertia 0.7, c1 = c2 = 1.5; velocity clamped at 20 % of each range. Particle 0 = the untuned IT2FIS.
Chart: Swarm convergence, 1 h (validation objective)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
global best | 1.1454 | 1.1497 | 1.1511 | 1.1519 | 1.1519 | 1.1519 | 1.1519 | 1.1519 | 1.1534 | 1.1534 | 1.1559 | 1.1559 | 1.1559 | 1.1559 | 1.1559 | 1.1559 | 1.1559 | 1.1565 | 1.1565 | 1.1565 | 1.1567
Validation objective 1.145 → 1.157; uncertainty-band scale 1.24.
Starting from the untuned system means PSO can only be chosen if validation data says it is better.
Notes: PSO answers Q2. The decision vector, objective and settings are fixed and documented. Because the untuned IT2FIS is one of the starting particles, PSO's validation score is at least as good by construction; only the test period can show whether that carries over.

## Slide 8: SOM: matching the river to learned prototype states
1
Learn prototypes (no labels)
Batch Kohonen SOM on standardised (level, rise, rain); grid size chosen on validation (8x8 for Bengalas, 1 h).
2
Give each node a level
The level with the lowest expected cost over the training states it won: missing a level costs 2, a false step up costs 1.
3
Decide
Find the closest prototype and report its level. The explanation names the prototype and its history.
Chart: Node 56: what training states on this node later became
| Normal | Low | Moderate | High | Critical
training states | 1 | 2 | 7 | 15 | 73
Node 56 is mapped to Critical: with 73 of 98 states Critical, that choice has the lowest expected cost.
Notes: The SOM is unsupervised: it only learns prototype states. Labels are used afterwards to give each node a level, with an asymmetric cost so rare High and Critical states are not outvoted by Normal. Node 56 is the node the flood example later in the deck lands on.

## Slide 9: ANFIS: a fuzzy system trained like a network
1
Membership
Gaussian MFs: 5 level, 4 rise, 4 rain
2
Rule firing
product of memberships, 80 rules
3
Normalise
w̄ = w / Σw
4
Rule output
p0 + p1·level + p2·rise + p3·rain
5
Sum
Σ w̄ · f → score 0–100 → level
Hybrid learning (Jang, 1993)
Each of 40 epochs: least squares for the 320 rule-output parameters, then one gradient step on the MF centres and widths.
Rare levels are up-weighted; ridge strength chosen on validation.
Finding: unconstrained training broke the meaning
On Malwathu, 'Elevated' moved below 'Normal' and widths collapsed, so explanations named the wrong terms. Centres now stay between neighbours and widths within 0.5–2×. Cost: Malwathu F1 0.83 → 0.66, reported, not re-tuned.
ANFIS learns from data but stays readable: every alert names its most active rules.
Notes: ANFIS uses the same 80 rule premises as the IT2FIS, so the two are directly comparable, but each rule's output is a learned linear equation. The interpretability constraint was motivated by wrong explanations, not by scores, and it lowered the Malwathu score. That trade-off is disclosed in the experiment protocol.

## Slide 10: Evaluation designed to prevent leakage
1
No leakage
Chronological split; all fitting on the training period; tuning on validation only; fit rows whose target falls in validation are purged; unit test: changing test data leaves every learned parameter unchanged.
2
Genuine metrics
Alert precision, recall, F1 with 95 % moving-block bootstrap intervals; five-level macro F1, κ, severity-weighted error; missed alerts and false alarms; fit and run time.
3
Simulated faults
9 scenarios (missing 10/30 %, noise ×3, stuck, conflicting rain, spikes, combined) × 3 seeds, injected into a copy of the test data; labels always from the original data.
Does the data support each forecast horizon? (Bengalas, test period)
Horizon | Labelled rows | Alert steps | Class changes vs now | New alert onsets | Verdict
30 min | 21,230 | 674 | 2.7 % | 46 | Supported
1 h | 20,904 | 653 | 4.7 % | 87 | Supported
3 h | 20,359 | 633 | 10.2 % | 223 | Supported
Malwathu: 30 min / 1 h / 3 h | — | — | — | — | Not supported (daily)
Notes: The horizon table is the data check behind offering 30 minutes, 1 hour and 3 hours: enough labelled rows, enough alert steps, and the class actually changes between now and the horizon, so the task is not trivial. The daily dataset cannot represent sub-daily horizons, so they are reported as unsupported rather than interpolated.

## Slide 11: Clean data: three techniques tie, SOM lags
Chart: Alert F1, 1 h ahead, Bengalas test period
| IT2FIS | PSO-IT2FIS | SOM | ANFIS | Threshold (ref.)
alert F1 | 0.88723 | 0.89437 | 0.73658 | 0.86676 | 0.86215
Model | F1 [95 % CI] | Precision | Recall | Missed | False alarms
IT2FIS | 0.887 [0.850, 0.915] | 0.866 | 0.910 | 59 | 92
PSO-IT2FIS | 0.894 [0.859, 0.922] | 0.901 | 0.888 | 73 | 64
SOM | 0.737 [0.665, 0.796] | 0.617 | 0.914 | 56 | 371
ANFIS | 0.867 [0.820, 0.902] | 0.830 | 0.907 | 61 | 121
Threshold (ref.) | 0.862 [0.820, 0.895] | 0.858 | 0.867 | 87 | 94
Intervals of IT2FIS, PSO-IT2FIS and ANFIS overlap, so none is significantly better. SOM's interval lies entirely below IT2FIS's. SOM raises 4× more false alarms.
Answer to Q1: IT2FIS 0.887, PSO-IT2FIS 0.894 and ANFIS 0.867 are statistically tied; SOM 0.737 is clearly weaker.
Notes: This is the main comparison: clean sensors, one hour ahead, on the held-out test period. The bracket is a 95 % moving-block bootstrap interval; whole days are resampled because neighbouring 30-minute steps are not independent. We only call a model better when the intervals do not overlap. The threshold rule is a reference: the labels are built from it.

## Slide 12: Skill falls with lead time for every model
Chart: Alert F1 by horizon, clean test data, Bengalas
| 30 min | 1 h | 3 h
IT2FIS | 0.93459 | 0.88723 | 0.66358
PSO-IT2FIS | 0.94404 | 0.89437 | 0.69463
SOM | 0.71305 | 0.73658 | 0.58198
ANFIS | 0.94489 | 0.86676 | 0.66241
0.935 → 0.664
IT2FIS F1 from 30 min to 3 h
10.2 %
of steps change level class within 3 h (2.7 % within 30 min)
+0.031
PSO's largest gain, at 3 h, still inside the interval
The further ahead, the less the current readings say; a linear level forecaster does not beat persistence either.
Notes: Persistence MAE vs ARX MAE: 30 min 0.0075 vs 0.0080 m; 1 h 0.0132 vs 0.0137 m; 3 h 0.0316 vs 0.0322 m. Better 3-hour skill would need more inputs, for example upstream gauges or rainfall forecasts.

## Slide 13: PSO: small gains, not statistically significant
Chart: Test alert F1, Bengalas
| 30 min | 1 h | 3 h
Untuned IT2FIS | 0.93459 | 0.88723 | 0.66358
PSO-tuned IT2FIS | 0.94404 | 0.89437 | 0.69463
92 → 64
false alarms at 1 h
59 → 73
missed alerts at 1 h
0.931 → 0.969
Malwathu validation objective, while test F1 stayed 0.864
Answer to Q2: PSO trades missed alerts for fewer false alarms; its gains stay within the confidence intervals.
Notes: PSO raises test F1 at every Bengalas horizon, but every pair of 95 % intervals overlaps (1 h: untuned [0.850, 0.915] vs tuned [0.859, 0.922]). On Malwathu the validation score rose but the test score did not move: a textbook sign of fitting the validation block.

## Slide 14: Faulty sensors: IT2 models hold up best
Chart: Mean alert F1 over 9 simulated faults, 1 h, Bengalas
| IT2FIS | PSO-IT2FIS | SOM | ANFIS
Reliability layer off | 0.7936 | 0.79125 | 0.49652 | 0.64936
Reliability layer on | 0.79858 | 0.79767 | 0.51897 | 0.69273
Where the reliability layer matters
Case (1 h) | Off | On
Spikes · IT2FIS | 0.755 | 0.821
Spikes · ANFIS | 0.651 | 0.750
Medium noise · ANFIS | 0.413 | 0.508
Clean · IT2FIS | 0.887 | 0.880
Missing 30 % · IT2FIS | 0.845 | 0.827
Fault detection recall of the reliability checks: missing 100 %, spikes 55 %, high noise 62 %, stuck 3 %, conflicting rain 1 %.
Answer to Q3: the layer clearly helps against spikes, costs a little on clean data, and misses stuck and conflicting sensors.
Notes: ANFIS collapses under noise (medium 0.413, high 0.186); we have not isolated why. SOM is the least robust overall. The reliability layer is not a free win, and the weak detection of stuck and conflicting sensors is a real limitation, shown openly on the website.

## Slide 15: A real alert, explained: 7 December 2022
Chart: Bengalas water level around the alert (alert issued 20:30)
| 05:30 | 06:00 | 06:30 | 07:00 | 07:30 | 08:00 | 08:30 | 09:00 | 09:30 | 10:00 | 10:30 | 11:00 | 11:30 | 12:00 | 12:30 | 13:00 | 13:30 | 14:00 | 14:30 | 15:00 | 15:30 | 16:00 | 16:30 | 17:00 | 17:30 | 18:00 | 18:30 | 19:00 | 19:30 | 20:00 | 20:30 | 21:00 | 21:30 | 22:00 | 22:30 | 23:00 | 23:30 | 00:00 | 00:30 | 01:00 | 01:30 | 02:00 | 02:30 | 03:00 | 03:30 | 04:00 | 04:30 | 05:00
recorded level (m) | 1.28 | 1.29 | 1.28 | 1.28 | 1.29 | 1.29 | 1.3 | 1.3 | 1.3 | 1.31 | 1.32 | 1.31 | 1.3 | 1.29 | 1.28 | 1.26 | 1.27 | 1.25 | 1.24 | 1.23 | 1.23 | 1.22 | 1.22 | 1.2 | 1.2 | 1.18 | 1.17 | 1.16 | 1.16 | 1.17 | 1.4 | 1.88 | 2.44 | 2.6 | 2.77 | 2.84 | 2.95 | 2.96 | 2.87 | 2.76 | 2.64 | 2.52 | 2.42 | 2.3 | 2.21 | 2.08 | 1.99 | 1.91
High threshold | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268 | 1.4268
Critical threshold | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161 | 1.7161
IT2FIS
Critical
PSO-IT2FIS
Critical
SOM
Critical
ANFIS
High
Threshold (ref.)
Moderate
IT2FIS: why Critical, 30 min ahead
Level 1.40 m (Elevated), between Moderate and High.
Rising +0.46 m/h; 22.6 rain in the last 2 h (Heavy).
Strongest rule: IF level Elevated AND rise Rising AND rain Heavy THEN Critical (firing 0.43–0.94).
Risk interval [85, 95] → 90/100 → Critical band.
Outcome: 30 min later (21:00) the level was 1.88 m → Critical. The level-only reference still said Moderate.
Notes: This is real test-period data, replayable on the Assess Risk tab. Thirty minutes before the river crossed the flood threshold, IT2FIS, PSO-IT2FIS and SOM issued Critical from the fast rise and heavy rain, ANFIS said High, and the level-only reference still said Moderate. Every bullet on the right is generated from the model's own internals.

## Slide 16: What the results do not show
!
Proxy labels
No recorded floods exist: scores measure agreement with a level-threshold rule, not real warning accuracy.
!
Simulated faults
Sensor failures are injected with fixed seeds; behaviour under real failures is untested.
!
Two catchments
Few large events; Malwathu has only 66 alert days in its test period, hence wide intervals.
!
PSO not proven
Gains are inside the confidence intervals; on Malwathu, validation rose while test did not.
!
ANFIS trade-off
Interpretability constraints cost accuracy on Malwathu (0.83 → 0.66).
!
Detection gaps
The reliability checks catch only 3 % of stuck and 1 % of conflicting-rain faults.
Notes: We state these limits before anyone asks. Two design changes were made after some test numbers had been printed (the uncertainty-band cap and the ANFIS constraints); both were triggered by defects rather than scores and are disclosed in the experiment protocol.

## Slide 17: Conclusions
Honest comparison beats a single winner
Q1
IT2FIS, PSO-IT2FIS and ANFIS are tied on clean data; SOM is clearly weaker.
Q2
PSO gives small, non-significant gains: fewer false alarms, more misses.
Q3
IT2 models are most robust to faults; the reliability layer helps mainly against spikes.
Next
Daily Indian check on CAMELS-IND; stuck-sensor detection; upstream inputs for 3 h.
Live demo: floodguard-ai-chi.vercel.app · Code: github.com/usha-sree7/FlowGuard
Notes: Close with the three answers and the next steps, then open the live demo: Assess Risk with the December 2022 episode, then Compare Models and the sensor-fault simulator.